DEP Sequence Control Tables:
=== ======== ======= ======

I. Normal Observation Table:
    
   Normal observation tables are loaded in the sequence buffer, at the high
   addresses. Only one table may be loaded at the same time. The DEP sequence
   copies the table to it's working registers. After the sequence has been
   initiated a new table may be loaded at any time. The new table is activated
   by setting the NEW Prime Table Flag (R64).
  
     Word #              Description
       1            Address of Prime60 observation list
       2            Address of Prime30 observation list
       3            Address of Alternate observation list
       4            ALT Header observation list address
       5            ALT Tail observation list address
       6            ALT Repeat Count
       7            ALT Cadence

II. Control Registers:

      Register           Description
        R64         New Prime Table available
        R65         ALT Enable Flag
        R66         Campaign Enable Flag
        R67         Campaign List Address
        R68         New Campaign List Flag
        R69         New Campaign List Address
        R70         Intra-Instrument Flag
        R71         Intra_Instrument List Address
        R72         Chain List Flag
        R73         Chain List Address



III. List Processing:

Campaign mode is implemented by a "List Processor" consisting of a set of
routines to initialize and return the address of the "next" observation on
each call.

The list format is shown below;

    Word #              Description
      0                 OBS List ID
      1                 OBS List Size

      2                 Campaign Header Observation 
      3                 Campaign Tail Observation
      4                 Campaign Prime Observation Address
      5                 Campaign Alternate Observation Address

      6                 Obs #1 Address
      7                 Obs #1 Repeat Count
      8                 Obs #1 IP Prog
      9                 Obs #1 OTP

     10                 Obs #2 Address
     11                 Obs #2 Repeat Count
     12                 Obs #2 IP_Prog
     13                 Obs #2 OTP
             ...
             ...
             ...
                        Obs #n Address
                        Obs #n Repeat Count
                        Obs #n IP_Prog
                        Obs #n OTP

The list can contain one level of nesting. A pair of words identify nested
lists. The first word contains size of the group. The repeat count of the
group is specified as a negative number.
OTP is the pointer to the offset table. This table contains image
co-ordinates indicate the region of interest. The size of the region is
chosen by the IP program.


IV. Observation List
 
  Observations consist of a series of frames, preceded by a 12 byte header.
  The header format is shown below;
 
       Byte No.            Description
 
         0                Number of Frames
        1-2               Observation ID
        3-4               Time of First Picture
         5                PAW Position and direction
         6                CAL1 Position and direction
         7                CAL2 Position and direction
        8-9               Spare


 The format of frame specification is shown below;
       Byte No.            Description
 
        0-1               Time relative to the time of first picture
         2                MTM1 Position (or Lookup index)
         3                MTM2 Position (or Lookup index)
         4                PAW, CAL1 and CAL2 Position indecies
                              Bits         Usage
                               0-1      CAL1 Index
                               2-3      CAL2 Index
                                4       CAL position "Don't Care" Flag
                               5-6      PAW Index
                                7       PAW position "Don't Care" Flag
         5                Image Type and Exposure Index
                              Bits         Usage
                               0-5      Exposure Index
                               6-7      Image Type (1X, 3X, Dark, NoPic)
        6-9               DMA words