<TITLE> DEP Sequence Instructions </TITLE>

<H1> DEP Sequence Instructions </H1>

<PRE>

 1. BEQ   R/&    R   R/I   Branch to OP1 if OP2 == OP3       00000ac0
 2. BNE   R/&    R   R/I   Branch to OP1 if OP2 != OP3       00010ac0
 3. BGT   R/&    R   R/I   Branch to OP1 if OP2 >  OP3       00100ac0
 4. BLT   R/&    R   R/I   Branch to OP1 if OP2 <  OP3       00110ac0
 5. BLE   R/&    R   R/I   Branch to OP1 if OP2 <= OP3       01000ac0
 6. BGE   R/&    R   R/I   Branch to OP1 if OP2 >= OP3       01010ac0
 7. BZ    R/&    R    -    Branch to OP1 if OP2 ==  0        011000a0
 8. BNZ   R/&    R    -    Branch to OP1 if OP2 !=  0        011010a0
 9. UBR   R/&    -    -    Branch to OP1                     011100a0
10. CLL   R/&    I    -    Call to OP1                       011110a0
11. DDC   R/I    -    -    Direct Device Command (1 Arg.)    100000a0
12. DDC   R/I   R/I   -    Direct Device Command (2 Arg.)    10001ab0
13. SET    R    R/I   -    OP1 <- OP2                        100100b0
14. ADD    R    R/I   -    OP1 <- OP2 + OP1                  100110b0
15. SUB    R    R/I   -    OP1 <- OP2 - OP1                  101000b0
16. CON    &     &   R/I   Configure; DMA & APU COntrol      101010c0
17. CO1    &     &    &    Configure; DMA, APU/TLM COntrol   10110000
18. CO2    &     &    -    Configure; DMA COntrol only       10111000
19. DFRM   R     -    -    Decode Observation Frame          10110010
20. IFRM  R/&    R    -    Open Frame List                   101101a0
22. XIPM  R/I    -    -    Execute IP Macro                  101101a0
23. SIPR  R/I   R/I   -    Set IP Register                   11000ab0
24. EXP   R/I    -    -    Set Exposure Time                 110010a0
25. SID    I     -    -    Set Sequence ID                   11010010
26. OPNL   R     &    -    Open Observations List            11010100
27. CLSL   R     -    -    Close Observations List           11011000
28. GLSQ   R     -    -    Get List Sequence Address         11011010
29. GALT   R     -    -    Get Alternate Sequence Address    11011100
30. GRT    R     -    -    Get Relative Time                 11100010
31. GIC    R     -    -    Get Interval Counter (Since SIC)  11100100
32. INC    R     -    -    OP1 <- OP1 + 1                    11100110
33. DEC    R     -    -    OP1 <- OP1 - 1                    11101000
34. CLR    R     -    -    OP1 = 0                           11101010
35. STS    -     -    -    Stop Sequence                     11110000
36. SRT    -     -    -    Set Reference Time                11110010
37. SIC    -     -    -    Clear & start interval counter    11110100
38. TAP    -     -    -    Take a picture                    11110110
39. TAD    -     -    -    Take a dark frame                 11111000
40. RET    -     -    -    Return from CLL                   11111010
41. TIM   R/I    -    -    Wait for Time Mark                111111a1

<PRE>

<HR>
<H2> Additional Sequence Instructions: </H2>

<PRE>

The following instructions are implemented by the linker using "hidden" 
registers.

1. The follwoing commands allow the MTM positions to be changed from the values
specified in an Optics Configuration Block (OCB). The instructions load new
values into a pair of registers which are added to the base positions when
the CON instruction executes. This avoids the need for a large number of OCB's
if the successive OCB's differ only in MTM positions and the new positions
can be derived from the old ones.

    i. Clear MTM Offsets: 
       Mnemonic:  CMO
       OpCode:    FE

       This instruction sets MTM offset registers to zero. 

   ii. Increment MTM Offsets:
       Mnemonic:  AMx { R / I}  { R / I }     ;where 1 <= x <= 4
       OpCodes:   AM1  -- C0
                  AM2  -- C2
                  AM3  -- C4
                  AM4  -- C6

       This instruction adds the specified increments to the MTM offset 
       registers. The first operand contains the increment for MTM1.

2. The following instruction provides a means of using the CON instruction
with different OCB's without providing a different OCB address on each call.

   Load Optics Configuration Block:
   Mnemonic:  LOC {R/&}
   OpCodes:   

   This instruction copies the OCB specified by the operand into a
   perdetermined area of the sequence buffer. The CON instruction is called
   with the address of the standard OCB. Prior to calling the sequence the
   LOC instruction can be used to load the standard OCB with the required OCB.

3. The CON instruction can be generalised further by providing the capability 
to specify different DMA Control Blocks without having to specify different
addresses. The following instructions implement this capability.

   i. Load DMA Block
      Mnemonic: LDM  { R / &}
      OpCodes:  

      This instruction loads the address of a set of DMA blocks into a special
      register. The CON instruction is called with the address of this 
      register instead of the address of a particular DMA block. The MSB of the
      address is set to indicate to the CON instruction that this is a pointer
      to the address of the DMA block rather than the address of the DMA block
      itself. Before returning, the CON instruction increments this address
      by 4 bytes (the length of the DMA block) so that it points to the next
      DMA block. On the next call to CON the new DMA block is used.

  ii. A new mnemonic for the CON istruction would be required to enable the 
      linker to set the MSB in the address field.

4. The above scheme can also be used with a set of OCB's. Where the address of 
the first OCB is copied into a special register and the ms bit set to indicate
that it was a pointer to the address of an OCB. 



Number   Mnemonic               
  1        CMO      Clear MTM Offsets         CLR R27 (MTMOR)
  2        AMO      Increment MTM Offsets     ADD R27 (MTMOR) s1*256 + s2
  3        LOC      Load OCB Address          SET R31 (OCBR)  &OCBADR
  4        LDM      Load DMB Address          SET R29 (DMBR)  &DMBADR
  5        OC+      Increment OCB Address     INC R31 (OCBR)
  6        OC-      Decrement OCB Address     DEC R31 (OCBR)
  7        DM+      Increment DMB Address     INC R29 (DMBR)
  8        DM-      Decrement DMB Address     DEC R29 (DMBR)
  9        DMD      Set DMB Autodecrement     SET R28 (DMBSR)  0
 10        DMI      Set DMB Autoincrement     SET R28 (DMBSR)  1
 11        OCD      Set OCB autodecrement     SET R30 (OCBSR)  0
 12        OCI      Set OCB autoincrement     SET R30 (OCBSR)  1

<PRE>
<HR>
<PRE>

DEP-SCR Instruction Codes:

/*           00 01 02 03 04 05 06 07 08 09 0A 0B 0C 0D 0E 0F     */
/* 00 */      1, 0, 1, 0, 1, 0, 1, 0, 0, 0, 0, 0, 0, 0, 0, 0,
/* 10 */      1, 0, 1, 0, 1, 0, 1, 0, 0, 0, 0, 0, 0, 0, 0, 0,
/* 20 */      1, 0, 1, 0, 1, 0, 1, 0, 0, 0, 0, 0, 0, 0, 0, 0,
/* 30 */      1, 0, 1, 0, 1, 0, 1, 0, 0, 0, 0, 0, 0, 0, 0, 0,
/* 40 */      1, 0, 1, 0, 1, 0, 1, 0, 0, 0, 0, 0, 0, 0, 0, 0,
/* 50 */      1, 0, 1, 0, 1, 0, 1, 0, 0, 0, 0, 0, 0, 0, 0, 0,
/* 60 */      1, 0, 1, 0, 0, 0, 0, 0, 1, 0, 1, 0, 0, 0, 0, 0,
/* 70 */      1, 0, 1, 0, 0, 0, 0, 0, 1, 0, 1, 0, 0, 0, 0, 0,
/* 80 */      1, 0, 1, 0, 0, 0, 0, 0, 1, 0, 1, 0, 1, 0, 1, 0,
/* 90 */      1, 0, 1, 0, 0, 0, 0, 0, 1, 0, 1, 0, 0, 0, 0, 0,
/* A0 */      1, 0, 1, 0, 0, 0, 0, 0, 1, 0, 1, 0, 0, 0, 0, 0,
/* B0 */      1, 0, 1, 0, 1, 0, 1, 0, 1, 0, 0, 0, 1, 0, 1, 0,
/* C0 */      1, 0, 1, 0, 1, 0, 1, 0, 1, 0, 1, 0, 0, 0, 0, 0,
/* D0 */      1, 0, 1, 0, 1, 0, 1, 0, 1, 0, 1, 0, 1, 0, 0, 0,
/* E0 */      0, 0, 1, 0, 1, 0, 1, 0, 1, 0, 1, 0, 0, 0, 0, 0,
/* F0 */      1, 0, 1, 0, 1, 0, 1, 0, 1, 0, 1, 0, 0, 1, 0, 1  };
<PRE>